121, 1.3i,, 1324 cc, 1991-, Engine Code B3,

Ignition data

121, 1.3i
Ignition system type: El-i
Ignition coil make/type: n / a
Supply voltage: 12 - Volts without ballast resistor
Primary resistance: 0.68-0.84 Ohms
Secondary resistance: 9600-14400 Ohms
Distributor make/type: n / a
Contact breaker gap/air: n / a mm
Dwell angle: n / a Deg
Ignition Timing - unleaded: 16  1/1100 Deg eng/rpm (without vacuum)
Ignition Timing - leaded: n / a Deg eng/rpm (without vacuum)
Timing mark location: Pulley
No 1 plug location: O/S/F
Firing Order: 1-3-4-2
Spark plug make: NGK
Spark plug type: BKR5E-11
Electrode gap: 1.0-1.1 mm

Fuel System

121, 1.3i
Fuel type: U Cat
Fuel pump type/pressure: Elec/2.4-2.8 bar
Engine idle speed: 1100-1150 rpm
Fast idle speed: n / a rpm
CO level at idle speed: 0.5 Max Vol %

Engine Data

121, 1.3i
Valve clearance - inlet: 0.30 h mm (hot)
Valve clearance - exhaust: 0.30 h mm (hot)
Compression pressure: 10.3-14.7 bar
Oil pressure: 2.9-3.9/3000 bar/eng/rpm
Radiator pressure cap: 0.74-1.03 bar/type
Drive belt 1 - size: 9.5x888 KDB888 mm/type
Drive belt 2 - size: n / a mm/type

Electrical System

121, 1.3i
Alternator output: 65/3000 Amps/eng/rpm
Regulated output: 14.1-14.7 Volts
Battery: 12/40 V/Ah
Starter motor make/type: Bo/0 001 114 015

Other data

121, 1.3i
Clutch operation type: n / a
Clutch adjustment: n / a mm
Cambelt failure: Damage
Cambelt Part Number: n / a
Tyre pressures: 2.0(28)f 2.0(28)r bar (psi)