626, 2.2i ,, 2184 cc, 1988-92, , Engine Code F2

Ignition data

626, 2.2i
Ignition system type: El-i
Ignition coil make/type: Han/-
Supply voltage: 12 - Volts without ballast resistor
Primary resistance: 0.72-0.88 Ohms
Secondary resistance: 10200-15200 Ohms
Distributor make/type: Mit/
Contact breaker gap/air: n / a mm
Dwell angle: n / a Deg
Ignition Timing - unleaded: 6  1/750 Deg eng/rpm (without vacuum)
Ignition Timing - leaded: n / a Deg eng/rpm (without vacuum)
Timing mark location: Pulley
No 1 plug location: O/S/F
Firing Order: 1-3-4-2
Spark plug make: NGK
Spark plug type: ZFR7A-11
Electrode gap: 1.0-1.1 mm

Fuel System

626, 2.2i
Fuel type: U Cat
Fuel pump type/pressure: n / a bar
Engine idle speed: 750  25 rpm
Fast idle speed: n / a rpm
CO level at idle speed: 0.5 Max Vol %

Engine Data

626, 2.2i
Valve clearance - inlet: Hyd
Valve clearance - exhaust: Hyd
Compression pressure: 7.8-11.2 bar
Oil pressure: 2.9-3.9/3000 bar/eng/rpm
Radiator pressure cap: 0.74-1.03 bar/type
Drive belt 1 - size: n / a mm/type
Drive belt 2 - size: n / a mm/type

Electrical System

626, 2.2i
Alternator output: 70/3000 Amps/eng/rpm
Regulated output: 14.1-14.7 Volts
Battery: 12/60 V/Ah
Starter motor make/type: Bo/-

Other data

626, 2.2i
Clutch operation type: Hyd
Clutch adjustment: 5-13/Pedal mm
Cambelt failure: Damage
Cambelt Part Number: F20312205 [F20212205]
Tyre pressures: 2.0(28)f 1.8(26)r bar (psi)